## Slide 1: Beyond Prefixes: The Power of Routing Policies and IRRs
Milad Afshari | CAPIF4 | Almaty, September 2025

## Slide 2: Who am I?
Milad Afshari
Enterprise Network Planning Manager @ MTN-Irancell(AS44244)
Co-founder & PC chair of IRNOG
PC member of CAPIF
Notes: اشاره به اینکه سال گذشته در مورد روتینگ سکوریتی ئر منطقه صحبت کردم. امسال تصمیم گرفتم با توجه به اینکه بهبود وضعیت امنیت روتینگ در آسیای مرکزی هنوز جا داره بهتر بشه بخصوص قزاقستان که درصد روآ ساین شده خیلی کمی داره، مجدد کمی پایه ای تر از اهمیت این موضوع صحبت کنم.

## Slide 3: Why This Talk?
Last year I spoke about routing security in the region. This year, since there is still room for improvement in Central Asia — including Kazakhstan — I decided to revisit the basics and highlight again why this topics matters:
  BGP has no built-in security mechanisms
  Misconfigurations and hijacks still happen
  Routing policies and IRRs help us bring order
  Goal: strengthen Internet resilience & security

## Slide 4: BGP at a Glance: Strengths and Challenges

## Slide 5: Internet Number Resources & BGP
The Internet relies on identifiers:
  IPv4 Addresses
  IPv6 Addresses
  Autonomous System Numbers (ASNs)
BGP:
  For nearly 30 years BGP has kept the Internet running, but it still faces security challenges. It was originally designed when the Internet was much smaller and based on a trust model between network operators

## Slide 6: BGP Routing Statistics

## Slide 7: The Problem with BGP
Prefix Hijacking: redirect traffic
Route Leaks: instability & misrouting
Misconfigurations: global outages
No built-in verification
Event | Explanation | Repercussions
Prefix/Route Hijacking | A network operator or attacker impersonates another network operator, pretending that a server or network is their client. | Packets are forwarded to the wrong place; this can cause Denial of Service (DoS) attacks or traffic interception.
Route Leak | A network operator with multiple upstream providers announces (often due to accidental misconfiguration) to one upstream provider that is has a route to a destination through the other upstream provider. | Can be used for traffic inspection and reconnaissance.

## Slide 8: BGP Incidents Overview
1997
2013
2008
2018
2024
Event: The issue started on June 27, when Eletronet S.A. (AS267613) mistakenly announced a very specific route (1.1.1.1/32) to its peers and upstream providers.
Impact: The incident impacted around 300 networks across 70 countries, though Cloudflare noted that the overall impact was relatively low and many users did not notice significant disruption.
1.1.1.1
Route Leak
Event: BGP hijacking led to DNS redirection and phishing of cryptocurrency wallets.
Impact: $17 million stolen from users due to compromised TLS connections.
MyEtherWallet Attack
Event: BGP-based man-in-the-middle attack targeting major US credit card companies and governments.
Impact: Interception of sensitive communications.
Belarus BGP MITM Attack
Event: Pakistan Telecom attempted to block YouTube locally but accidentally propagated the block globally.
Impact: Global internet access to YouTube was disrupted.
Pakistan Telecom and YouTube
Event: Software bug led to a large part of IP address ranges being misannounced as originating from AS7007.
Impact: Traffic was redirected and overwhelmed AS7007’s equipment, causing widespread disruption.
AS7007 Incident

## Slide 9: IRR (Internet Routing Registry)

## Slide 10: Internet Routing Registry (IRR)
IRR - the Internet Routing Registry
Public routing policy databases
  Used to register routing information
  Declaration of BGP announcements, connected peers and routing policies
Many IRR databases exist
  Mostly mirroring each other
  RIPE, APNIC, RADB, JPIRR, Level3, NTTCom, etc.
https://irr.net/

## Slide 11: Why register routing information?
Document your routing policy
  Associate network prefixes with an origin AS
Helps to filter unauthorized announcements
  Mitigates route hijacks and denial of service
Many transit providers and IXPs require it
  They build their filters based on the Routing Registry

## Slide 12: The RIPE Routing Registry
The RIPE IRR is a subset of the RIPE Database
Used for registering routing policy information
Includes several objects
  route(6), aut-num, filter-set, route-set, …
The RIPE Routing Registry is a part of the global IRR system

## Slide 13: IRR Objects
route / route6: prefixes
aut-num: AS & policies

## Slide 14: route(6) objects
Contains routing information for IPv4/IPv6 address space
Specifies from which AS a certain prefix may be originated
Used for creating BGP filters

## Slide 15: BGP Routing Policy

## Slide 16: What is a Routing Policy?
Who are your BGP peers? Which ASes?
What is your BGP relationship with them?
  Customer, Provider, Peer
What are your routing decisions?
  Which prefixes to accept?
  Which prefixes to announce?
  Which prefixes will be preferred in case of multiple routes?

## Slide 17: RPSL Language
RPSL - Routing Policy Specification Language
Allows network operators to specify their routing policies
  Generic way to describe BGP configuration in the IRR
  Not vendor-specific
Originated from a RIPE Document (RIPE-181)
Can be translated into router configuration
RFC 2622 - Routing Policy Specification Language RFC 2650 - Using RPSL in Practice

## Slide 18: Routing Policies in Practice
Notes: - With Providers: announce only customer routes
- With Customers: accept their prefixes
- With Peers: exchange only customer routes

## Slide 19: IRRs & BGP Automation
Tools available that get the policy data from the IRRs
  Extract prefixes from route(6) objects
  Query the IRRs over Whois protocol
Some can generate complete router configurations
Most are open source tools
Generating a Prefix Filter:

## Slide 20: RPSL tools for BGP automation
IRRToolset (written in C++)
  https://github.com/irrtoolset/irrtoolset
Rpsltool (perl)
  https://github.com/rfc1036/rpsltool
IRR Power Tools (PHP)
  https://github.com/6connect/irrpt
bgpq4 (C)
  https://github.com/bgp/bgpq4
Filtergen (Level 3)
  - https://github.com/anchor/filtergen
  - whois -h filtergen.level3.net RIPE::ASxxx
bgpq4 example

## Slide 21: IRR Limitations
IRRs may contain conflicting data
  Distributed databases that mirror each other
No central authority
  Who will verify the accuracy of the data?
No verification of holdership
  In some IRRs, you can create objects without checks
Not updated properly
  Information is missing, outdated or incorrect
Notes: 43 IRR filters are good only if the IRR entries are correct!

## Slide 22: RPKI
Verifies the association between resource holders and their Internet number resources
Attaches digital certificate to IP addresses and AS numbers
  RPKI is based on an X.509 certificate profile defined in RFC3779.
Only ~50% of IPv4 covered by RPKI
IRR still critical for remaining space
Dual use = best security today

## Slide 23: ROA data by Country (%)

## Slide 24: Conclusion
RPKI (ROA/ROV) is the most effective defense against accidental BGP hijacks and origin leaks. Steps for success:
  Creation of ROAs (Route Origin Authorizations).
  ASes (Autonomous Systems) rejecting routes inconsistent with ROAs.
The most effective security approach today is the combined use of IRR and RPKI
IRR provides broad, policy-based filtering and operational transparency
RPKI adds cryptographic validation of prefix ownership where available
This dual strategy ensures wider coverage, stronger accuracy, and better protection against routing threats
Together, they significantly enhance the resilience and security of the global Internet

## Slide 25: References
https://ripe.net
https://academy.ripe.net
https://iana.org
https://irr.net
https://www.kentik.com/blog/a-brief-history-of-the-internets-biggest-bgp-incidents
https://academy.ripe.net
https://stat.ripe.net
https://labs.apnic.net/measurements

## Slide 26: Thank you! Any Questions?
سپاسگزارم!
سوالی هست؟
Спасибо! Есть вопросы?