## Slide 1
QoS and DDoS mitigation in IXP
RIPE NCC Days Sofia, 28 June 2023

## Slide 2
Different traffic treatment for different services
Quality of Service
What it has to do in neutral IXP infrastructure
Best-effort - default
Assured forwarding - reserved bandwidth
Expedited forwarding - low latency (priority)
Network Control - priority and reserved bandwidth
Input classification and output queueing

## Slide 3
Best effort for everything
Network Control for BGP (and ARP)
QoS on Peering only Member port
Output Queueing

## Slide 4
Best effort for Peering
Network Control for BGP
Expedited forwarding for Multicast
QoS on Peering + Multicast
Multicast is used for real-time Audio/Video transport
Highly sensitive for packet loss and variable delay (jitter)
Output Queueing

## Slide 5
Best effort for Peering
Network Control for BGP
Expedited forwarding for Multicast Assured forwarding for Private VLANs
QoS on Multi-service Member port
Private VLANs normally carry more important traffic than peering
Output Queueing

## Slide 6
Best effort for possible DDoS
Assured forwarding for other Peering
Network Control for BGP
Expedited forwarding for Multicast Assured forwarding for Private VLANs
QoS with DDoS mitigation
Reserve zero bandwidth for possible DDoS traffic
Output Queueing

## Slide 7
Congestions on Member ports
Routing change
  policy
  public peering as backup of private peering
Increased traffic
  live events
  software updates
DDoS attacks

## Slide 8
PMacct ElasticSearch
Zabbix
Detecting Congestion Cause
SFlow / Port Mirroring

## Slide 9
Low-and-Slow DDoS attack
  protocol and application layer
High packet rate DDoS attacks
  TCP syn, DNS, HTTP/S
  spoofed traffic
Solutions: hardware/software solutions, BCP.38
Volumetric DDoS attack
overflow transport links to the victim
Amplification
Bot networks
DDoS Attacks

## Slide 10
DDoS Patterns
Application | Protocol | Port
Invalid | UDP | 0
Chargen | UDP | 19
DNS | UDP | 53
NTP | UDP | 123
SNMP | UDP | 161
U Discovery | UDP | 10001
Memcache | UDP | 11211
SSDP | UDP | 19000
Amplification
Request from spoofed IP address of the victim
Large response to target
Most attacks last less than 2 minutes Multiple protocols

## Slide 11
Classify UDP with source 53 exceeding 50 Mbps on all ports as potential DDoS
DNS DDoS attacks
DNS is important but low bandwidth traffic
(Less than 10 Mbps on whole IXP)
Multiple Gbps during attack
Solution: Policing
Same solution for other patterns

## Slide 12
DDoS attack w/o congestion

## Slide 13
DDoS attack causing congestion

## Slide 14
Real Attack in Monitoring
DDoS Queue Dropped in pps
DDoS Queue Queued in pps

## Slide 15
Real Attack in Monitoring
Peering Queue Queued in pps
Peering Queue traffic in Gbps
Peering Queue Dropped in pps - 0

## Slide 16
DDoS
Solution
Peering;
Pros & Cons

## Slide 17
DDoS solution pros
Always on, works for shot time frame attacks
Whole network protected, including core links
Dot1p mark on output traffic
+

## Slide 18
DDoS solution cons
Minimal possibility for classifying useful traffic as DDoS
Zero-day DDoS Attacks
Output Queue on Reseller ports
(Applied on port not VLAN)
Remote Peering Ports with lower speed than port speed
-

## Slide 19
DDoS solution future development Ideas
Whitelisting
Calculate IP Address reputation
Per-VLAN queueing on Carrier/Reseller ports
Port speed shaping (Member configured in my.bix.bg)
-

## Slide 20
Thank you!
Peering;
www.BIX.BG
harry@bix.bg
Q&A