## Slide 1: netlab Bringing the joy back to virtual networking labs
Ivan Pepelnjak (ip@ipSpace.net) Network Architect ipSpace.net AG

## Slide 2: Who is Ivan Pepelnjak (@ioshints)
Past
  Kernel programmer, network OS, and web developer
  Sysadmin, database admin, network engineer, CCIE
  Trainer, course developer, curriculum architect
  Team lead, CTO, business owner
Present
  Network architect, consultant, blogger, webinar, and book author
Focus
  SDN and network automation
  Large-scale data centers, clouds, and network virtualization
  Scalable application design
  Core IP routing/MPLS, IPv6, VPN
Also: I built too many labs for one lifetime, and hated that with passion

## Slide 3: Based on a True Story
That should be trivial to test in a lab… However, someone has to build that lab…
R1
R2

## Slide 4: The Reality Intervenes…

## Slide 5: A Networking Lab Is Much More than Topology
Add network services
Design and implement routing protocols
(Optional) Create virtual interfaces
Deploy initial device configurations
Create addressing plan
Build the lab topology

## Slide 6
And now for something completely different

## Slide 7: What Do We Need (in Unicorn Land of Infrastructure-as-Code)
Create a high-level description of the network
  Two devices: R1 and R2
  Let’s make them Arista EOS containers
  They are running OSPF
  We need four links (two of them stub LANs)
  Oh, we’re running unnumbered links…
Next
  Save the file
  Execute netlab up and you’ll get a running network (including IP addressing and OSPF)
topology.yml
nodes: [ r1, r2 ]
defaults.device: eos
provider: clab
module: [ ospf ]
links: [ r1, r2, r1-r2, r1-r2 ]
addressing.p2p.ipv4: True
R1
R2

## Slide 8
  Create configuration files
  Start the containers
  Start an Ansible playbook
  Initial device configuration
  Configuring OSPF
  Connect to the device
  … and we have the answer!

## Slide 9: Wait, What Just Happened? netlab up Behind the Scenes
netlab create
Start the lab
Adjust networking infrastructure
Prepare virtual infrastructure
Data model transformation
Snapshot
CLI arguments
Topology file
Plugins
Modules
Defaults
Orchestrator configuration
Ansible inventory
netlab initial
Ansible playbook
Custom configuration templates
System configuration templates

## Slide 10: Building a Networking Lab with netlab
Add network services
Design and implement routing protocols
Create virtual interfaces
Deploy initial device configurations
Create addressing plan
Build the lab topology
Initial netlab use case
Built-in and custom IPv4 + IPv6 address pools (loopback, P2P, LAN, VLAN, VNI, tunnels), DHCPv4/v6
Jinja2 configuration templates + Ansible plays for 20+ platforms
VLAN, VRF and VXLAN configuration modules
OSPF, IS-IS, EIGRP, BGP, MPLS configuration modules
EVPN, MPLS/VPN, 6PE configuration modules

## Slide 11: Every Lab Is Special
Add network services
Design and implement routing protocols
Create virtual interfaces
Deploy initial device configurations
Create addressing plan
Add custom configuration
  Static configuration templates
  Configuration templates modifying built-in configurations
  Multi-vendor and multi-platform support
Modify data transformation with plugins
  Modify the built-in transformation rules
  Add new functionality (example: IP anycast)
  Add new attributes or functionality to existing configuration modules (example: BGP allowas-in)
Build the lab topology

## Slide 12: Current State of netlab (April 2024)
Network devices
  Arista vEOS/cEOS
  Aruba CX
  Cisco ASAv, IOSv, IOS XE (CSR), Nexus OS (9300v), IOS XR/XRd
  Cumulus Linux 4.x and 5.x (NVUE)
  Dell OS10
  Fortinet
  FRR
  Juniper vSRX 3.0, vMX, vPTX (vEVO)
  Mikrotik RouterOS 6 and 7
  Nokia SR Linux and SR OS
  VyOS 1.4
Hosts and daemons
  Generic Linux host or container
  BIRD
  dnsmasq
Virtualization providers
  KVM with libvirt (Vagrant)
  Docker (containerlab)
  Hardware labs (requires extra interface information)
  VirtualBox (Vagrant) (deprecated)
Multi-provider topologies
  Combine containers and virtual machines in the same lab
  Connect external devices with the virtual lab

## Slide 13: Current State of netlab: Behind the Scenes
Network devices
  Arista vEOS/cEOS
  Aruba CX
  Cisco ASAv, IOSv, IOS XE (CSR), Nexus OS (9300v), IOS XR/XRd
  Cumulus Linux 4.x and 5.x (NVUE)
  Dell OS10
  Fortinet
  FRR
  Juniper vSRX 3.0, vMX, vPTX (vEVO)
  Mikrotik RouterOS 6 and 7
  Nokia SR Linux and SR OS
  VyOS 1.4
The Heroes | 
Stefano Sasso | Jeroen van Bemmel
Aruba, Junos, Dell OS10, Mikrotik, VyOS | FRR, Nokia SR Linux, Nokia SR OS

## Slide 14: Current State of netlab (April 2024)
Addressing
  IPv4 + IPv6
  Address pools + static prefixes
  VLAN-wide subnets
  Static interface addresses
  Unnumbered IPv4 and IPv6 (LLA) interfaces
  Layer-2-only interfaces
  DHCP (clients, servers, relays)
Data Plane
  VLANs and VRFs
  VXLAN (static ingress replication or EVPN)
  MPLS including SR-MPLS
  SRv6
  Tunnel interfaces
Routing Protocols
  OSPFv2 and OSPFv3
  IS-IS
  EIGRP
  BGP
  BFD
  VRRP and anycast gateways
MPLS Control Plane
  LDP, BGP-LU, SR-MPLS (OSPF or IS-IS)
Network Virtualization
  MPLS L3VPN and 6PE
  EVPN (bridging, VLAN bundles, asymmetric and symmetric IRB, most combinations of IGP and BGP)

## Slide 15: Sample Platform Support
More @ https://netlab.tools/platforms/

## Slide 16: But Wait, There’s More
External Connectivity
  Macvtap libvirt interfaces
  Macvlan container interfaces
  Port forwarding for VMs and containers
External Tools
  SuzieQ
  Graphite
Ease-of-use
  Wiring, addressing, OSPF, and BGP reports (text, Markdown, HTML)
  Graphs (Graphviz or D2)
  Graphite GUI 🎉 🎉 🎉
  Automated validation
  Multiple lab instances on a single server
  Restore previous configurations
Large topologies
  Topology templates
  Staggered device start
  Link groups

## Slide 17: Example: Graph (D2)

## Slide 18: Example: Addressing Report (BGP)

## Slide 19: Example: Graphite GUI

## Slide 20: Example: Network Validation

## Slide 21: Deployment Scenarios

## Slide 22: Recommended: Ubuntu, KVM, libvirt, Docker
Prerequisite software
  Python3
  Ansible (to configure the devices)
Devices as virtual machines
  KVM
  libvirt
  Vagrant with vagrant-libvirt plugin
Containers
  Docker
  Containerlab
Linux (Ubuntu)
netlab CLI
Vagrant / containerlab
Ansible
KVM / Containers
Linux bridge
libvirt / Docker

## Slide 23: Use Existing x86 Device: Ubuntu VM
MacOS / Windows / Linux
Requirements
  You can run containers with any VM virtualization product
  Nested virtualization is required to run network device VMs
Virtualization solution with nested virtualization
  Hyper-V (WSL)
  KVM
  VirtualBox
  VMware Workstation/Fusion
Optional
  Start the VM with Vagrant (simplifies the operations)
Alternative
  Cloud deployment
Vagrant
VirtualBox or VMware Workstation/Fusion

## Slide 24: Ubuntu VM on Apple Silicon
MacOS (ARM CPU)
  multipass starts an Ubuntu VM on an ARM CPU
  Nested virtualization is not supported  containers only
  Container images must be built for the ARM CPU  FRRouting only (at the moment)
Interesting use cases
  Run BGP, VXLAN, or EVPN labs on your Apple laptop
  FRRouting control-plane configuration syntax is pretty close to the industry standard CLI
Multipass

## Slide 25: Some Assembly Required (Thank You, Vendors)
Automatically downloadable images and containers
  FRR
  Cumulus Linux
  Nokia SR Linux
  VyOS
Easy to download
  Juniper vPTX (no registration required)
Most everything else (from bad to worse)
  Registration (Arista EOS, Cisco Nexus OS)
  Download tied to a valid support contract
  Begging your SE
  Available only if you know the right dev person

## Slide 26: But Wait, That’s Not All
After you download a container image (Arista cEOS)
  Unpack and install it (easy)
Virtual machines are a nightmare
  Download a virtual disk
  It boots without a configuration and expects stuff on serial port
  Exception: Junos and ASA can take configuration from a mounted CD-ROM
Building a Vagrant box
  What we need to automate lab startup
  Start the VM, answer a dozen questions
  Copy-paste initial configuration
  Save the configuration, shut down the VM
  Package as a Vagrant box, hope it works

## Slide 27: Getting Started

## Slide 28: Getting Started: Hardware
Get decent hardware
  Network devices consume between 256MB (Mikrotik) and 12GB (Cisco Nexus 9300v release 10.3) per node
  Containers consume between 200MB (FRR) and 1GB (Arista cEOS, Nokia SR Linux)
Decide which deployment architecture you want to use
  Existing x86 hardware using Windows/Mac: Linux VM (might need nested virtualization support)
  ARM CPU: Linux VM running FRR containers
  Standalone Linux server on dedicated hardware: use a fresh copy of Ubuntu
Standalone server recommendations
  Intel NUC works great (but is no longer available)
  Run containers (Arista, Cumulus, FRRouting) on a VM in the cloud (example: Oracle Cloud Free Tier)
  Some cloud providers offer nested virtualization (Google Cloud, Packet, Digital Ocean)

## Slide 29: Getting Started: Installation
Ubuntu
  Start with a (fresh) Ubuntu VM or a bare-metal server
  Install Python3 if needed
  Install networklab package with pip
  Use netlab installation scripts to install libvirt/KVM, Vagrant, Ansible, Docker, containerlab…
  Download or build Vagrant boxes or containers (tons of recipes on netlab.tools/labs/libvirt and netlab.tools/labs/clab)
Other Linux distributions
  Everything should work (apart from installation scripts)
  Box-building tools have been tested on Ubuntu
  We won’t be able to help you 🤷‍♂️

## Slide 30: Is It Worth It? What Others Are Saying…

## Slide 31: What Others Are Building with netlab

## Slide 32: How Can You Help?
  Spread the word ;)
  Use the tool to build your labs
  Ask questions and report bugs
Want to contribute?
  Fix documentation
  Fix bugs
  Add new functionality to existing devices (example: VXLAN on IOS XR or vPTX)
  Add new devices
Still not enough?
  Develop new plugins (hint: OSPF interface parameters)
  Develop new modules (IP multicast, Babel, RIP…)

## Slide 33: Questions?
Netlab resources
Documentation: netlab.tools
Blog posts: blog.ipspace.net/tag/netlab.html
Source code: github.com/ipspace/netlab
Examples: github.com/ipspace/netlab-examples
Sample project: bgplabs.net
To reach me
Web: ipSpace.net
Email: ip@ipSpace.net
Use GitHub issues / discussions to ask netlab questions and report challenges

## Slide 34: netlab High Level Architecture

## Slide 35: High-Level Architecture
netlab CLI
Vagrant
Containerlab
Ansible
VirtualBox
libvirt
KVM
Docker
Topology file
Plugins
System defaults

## Slide 36: Data Transformation and Configuration File Creation
Data model transformation
Snapshot
CLI arguments
Topology file
Plugins
Modules
Defaults
Orchestrator configuration
Ansible inventory
External tool configurations

## Slide 37: netlab initial – Device Configurations
Ansible playbook
Device-specific configuration
Ansible inventory
Custom configuration templates
System configuration templates
Module-specific configuration
Module-specific task list