## Slide 1: Latency Characterization of Public Cloud Service Platforms
Rita Ingabire, Antonio Bazco-Nogueras, Vincenzo Mancuso, Luis M. Contreras and Jesus Folgueira

## Slide 2: AGENDA /OVERVIEW
Motivation
Measurement Campaign
Results
  Characterization
  Forecasting
Conclusions
Notes: Lets set out the agenda for this talk
Four main parts –
Motivation for work
Measurements took,
Results,
And conclusions and some takeaways
lets start with the motivation

## Slide 3
Why are internet users always in the clouds? collaboration, data backups, entertainment
Why is the cloud of interest to Infrastructure Providers? New Killer-apps for next generation of cellular networks
- Latency Constrained
- Computationally demanding
- Connection to public networks
Autonomous vehicles, Extended Reality etc
Motivation
Notes: Users are always in the cloud : entertainment, real-time collaboration, and secure data backup.
Therefore their providers must support this and other new apps like immersive reality, autonomous devices, and industrial applications.
New services must be ultra Low latency, requre computational power, constant web connectivity since they most likey will be in the clouds

## Slide 4
Goal: Understanding Cloud latency
What are the characteristics of the cloud latency w.r.t. time, location, or type of service?
Can we forecast the future state of the network?
Can we understand the results?
  through explainable algorithms
  Are complex AI algorithms required?
Motivation
Notes: What does the Network Provider need to understand about the cloud?
Goal: Characterizing cloud performance
  Does the cloud location matter?
  Does the cloud owner matter?
  Can we predict latency , with what accuracy ?
  Can we understand results ?
. So that they can -
  Plan network management in advance
  Detect route anomalies and make modifications

## Slide 5: AGENDA /OVERVIEW
Motivation
Measurement Campaign
Results
  Characterization
  Forecasting
Conclusions
Notes: We move on to the next part - the measurements
Are we okay so far?

## Slide 6
Platform – RIPE ATLAS
RIPE : Internet Registry for Europe, the Middle East, Central Asia.
ATLAS is RIPE’s active measurement platform.
It allows different types of measurements:
  Ping
  Traceroute
  DNS
  SSL
  HTTP
  NTP
Notes: Is everyone familiar with ripe atlas?
Our campaign was carried out on ATLAS an active measurements platform run by RIPE
ATLAS allows 6 types of network measurements
For this work we used the traceroute measurements

## Slide 7: Platform – RIPE ATLAS
A) Credit System
Earn credits and Spend credits
B) Measurements
publicly available at RIPE Atlas Measurements
C) Tools
Magellan: Command Line Interface Toolset
Sagan: Measurement Parsing Library
Cousteau: Python client for the API
…………………… many others
Probe
Notes: How does ATLAS work.
To participate , install a probe , accumulates credits , take measurements
A lot of measurements are public except a few
ATLAS provides cmd tools , a measurement library and an API for interacting with the measurements

## Slide 8: Measurement Campaign – Destinations
Geographic area of Interest: Spain
Probes cover >92% of >40 million Internet users in Spain
224 active probes in Spain
Goal: Characterization of cloud ==> Single ASN IO (Telefónica)
  Remove impact of different IOs
Stable probes: Probes that have been:
  online at least 99% of last week before campaign,
  online at least 99% of last month before the campaign,
  and online at least 80% of the time since they were registered in RIPE Atlas
  36 probes (32 eventually )
Notes: This campaign was carried out in Spain
For a single Provider Telefonica
Ideal , Telefonica has over 200 probes (destination), covering most of country
Conditions – Filtered probes that had been online for over 99% of the month before we launched the measurements – 36 in total – eventilly 32 because 4 mostly returned timeouts

## Slide 9: Measurement Campaign - Cloud regions
  8 cloud servers from:
    AWS, Azure, Google Cloud, Telefónica
  From cloud to end user probes
    Install probes in the cloud regions
  Granularity:
    For 3 months (Jan. 30--Apr. 24, 2024)
    Every 30 minutes
    For the 32*8 = 256 links
    >4000 TR measurements per link
Notes: For the cloud, we chose 8. cloud providers installed probes in them
Experiment run for 3 months with traceroutes every 30 mins from these cloud probes to the Telefonica probes
> 4000 measurements

## Slide 10: Measurement Campaign – Cloud regions
  Geographic distribution:
  5 cloud probes in Spain
    4 Madrid
    1 Zaragoza
  3 cloud probes in France
    Paris
  Ownership distribution:
  3 probes in C1
  3 probes in C3
  1 probe in C2
  1 probe in Telefónica
Notes: Some further
5 in Spain and 3 in Paris because Azure didn’t have a presence in Spain and nearest was Paris
We were asked to anonymise the cloud ownership ie C1(AWS), C2( Azure) and C3 (Google )

## Slide 11: AGENDA /OVERVIEW
Motivation
Measurement Campaign
Results
  Characterization
  Forecasting
Conclusions
Notes: Okay now lets analyse the results from the measurements
_ when we xterise we are trying to answer some questions
A) Is the latency stable or variable ?
B) What are the latency bounds for a given source and destination?
C) Does knowing the distinct IPPATH taken aid you in estimating the final latency ?

## Slide 12: Characterization – Are there daily patterns?
Notes: Is the latency stable or variable ? – to answer that we examine the daily patterns
cluster all the measurements based on the hour of the day and plotted the mean, median, and 90th percentile each hour of the day over 3 months
Observations
remarkably constant across hours and cloud regions
increases during peak hours of the day
Peak change is only of around 1 or 2 ms

## Slide 13: Characterization - RTT CDF per Cloud Region
Notes: What are the latency bounds for a given source and destination?
CDF of traceroute for each cloud points aggregated over all the destinations
Observations
Most of the clouds can be reached within 50ms from all the destinations
Steep silhouette – rtt values are in a small range
Over all the destinatios the three servers in France are the ones with higher RTT
No difference in premium and standard tiers for cloud provider (c3)

## Slide 14: Characterization – RTT CDF per link
CDF from IOint to every destination probe
Highlighted: Probes that occupy the
  10th (blue)
  50th (green)
  90th (red)
percentile of mean RTT among the 32 probes
Notes: Also if we Pick a single cloud and look at all 32 destination
We see a few things
Observations
the individual CDFs are even steeper than the aggregated one - again stability
rtt in a very narrow range of around 5 ms, (others similar)
Deviant probes are in the Canary Islands - the farthest destination probe from this cloud

## Slide 15: Characterization – Insights !
  Time of the day does not matter
    No daily patterns
  Distance is decisive
Notes: Key takeaways so far from the latency characteristics :-
Time of the day does not matter
Further you are away from the cloud the higher your latency

## Slide 16: Characterization - Impact of distance
Fitting line:
2ms/100km + min. delay of 8.45 ms.
=> +15 ms from Madrid to Paris
Notes: Quantitatively what is the Impact of distance ?
Plot the mean RTT for each source-destination pair against distance
Use the least squares method to plot a regression line
Observations
RTT. increases about 2 ms per 100 km with a minimum delay of 8.45 ms.

## Slide 17: Characterization - Impact of ROUTE
Notes: Does knowing the distinct IPPATH taken aid you in estimating the final latency ?
We look at a single probe destionation pair
For a single probe destination pair (C1sp to probe 1003090) .
First plot the rtt src dst for each route
We see latency changes according to the path taken

## Slide 18: Characterization - Impact of ROUTE
Notes: Box plot for all the routes with 1% of the samples for same pair we can see that the
unique path matters even more
- Fastest path has mean rtt of 19.5ms and longest 24.5ms
- Therefore diff of 5ms
On average the most popular paths have mean rtt of 23.5ms
While not a very big difference something to consider while planning network paths

## Slide 19: Characterization – Insights II
  Time of the day does not matter
    No daily patterns
  Distance is decisive
  Route is decisive
    RTT Std. dev. over all samples = 2x avg. std. dev. per specific path
    the specific IP path does impact the latency
    path stability can reduce RTT variability
Notes: Another set of takeaways at this point is are :-

## Slide 20: AGENDA /OVERVIEW
Motivation
Measurement Campaign
Results
  Characterization
  Forecasting
Conclusions
Notes: Next we take a look at forecasting
Are there any questions at this point

## Slide 21: Forecasting
Time series: Can we forecast the future RTT performance based on the previous values?
Link quality estimation: Can we predict the performance for a new link from the known connections?
Can we infer which features are more important?
Notes: The measurments can be formatted as a timeseries
In which case we can use two types of algos for predictions
Time series forecasting methods use only previous latency
Supervised ML methods for spatial forecasting using all features available in the measurement
After forecasting can we use XAI to tell which features are important ?

## Slide 22: Forecasting – Time series
Simplest algorithms perform the best !!
Notes: We used a number of time series algos
Observations /TA
Best performing methods were naïve forecast , followed by Exponential smoothing
For ARIMA to perform well you need a lot of computational power
With better tuning LSTM can perform well
This was a simple 3 layer lstm
Latency is quite constant, with spare leaps that are not always predictable
Prophet is a time series forecasting library that decomposes data into trend, seasonality and holiday components using an additive or multiplicative model, with automatic handling of missing values, outliers and changepoints.
LSTM (Long Short-Term Memory) networks are specialized neural networks designed for sequential data that use memory cells and gates (input, forget, output) to learn long-term dependencies in time series data, making them effective for forecasting but requiring significant data and computational resources.
Alpha (α): The smoothing factor or level smoothing parameter
  Controls how much weight is given to recent observations vs historical values
  Value between 0 and 1
  Higher α means more weight on recent data
  Lower α means more weight on historical data
Beta (β): The trend smoothing parameter
  Used in double exponential smoothing (Holt's method)
  Controls how much the trend component is smoothed
  Value between 0 and 1
  Higher β means trend responds faster to changes
  Lower β means more stable trend estimates

## Slide 23: Forecasting - Spatial analysis
Forecast Variable : Latency
Notes: Our forecast variable will be latency
Our features are all features available in tracert measurement and the probe object

## Slide 24: Forecasting - Spatial analysis
Durations : ~ 70 days
Test/Train Split – 80/20
Percentage nans : 3.661839 %
Percentage last hop 255: 19.776974 %
Percentage with rtt > 100ms : 2.226213 %
Notes: To keep in mind

## Slide 25: Forecasting – Spatial analysis
Can we predict performance from monitored links?
Two cases:
  distance as sole feature
  All features are considered
Six algorithms:
Notes: we chose Two feature cases
Case were distance only
Case with all features
ANd these are the results : -
Observations
Tree based methods performed best
With distance alone you can get quite good results
Improved when all features considered

## Slide 26: Forecasting – Explainability
Can we evaluate what are the most important parameters?
  Two methods:
    LIME: Local Interpretable Model-agnostic Explanations
    SHAP: Shapley Additive Explanations
  For the two best models: XGBOOST and Random Forest
Notes: which features mattered we use LIME and SHAP
the most commonly used posthoc Explainable algoithms
On best performing
Observations
Distance is most important
Other features way less important
Next features is also important but its an order of importance less

## Slide 27
Can we access killer apps everywhere if they are in the cloud?
Conclusions and take-away messages
Notes: In conclusion
Can the providers users access their apps anywhere in the cloud ?
It depends - which apps work comfortably with rtt of 20ms ?
Probably not the new killer apps the network provider wants to provide in XR , Autonomous vehicles

## Slide 28: Conclusions and take-away messages
No daily patterns  similar to (Palumbo 2021)
No difference between premium and standard network service  differs from (Mok 2021)
Can we play cloud gaming everywhere? XR?  NO
  Cloud needs to be close. Distance is crucial.
  Strong support for Edge Services
Achieving the goals of B5G networks depends on external factors
Cloud developments depend on public networks  lack of control
F. Palumbo et al., “Characterization and analysis of cloud-to-user latency: The case of Azure and AWS,” Computer Networks, vol. 184, p. 107693, 2021 R. K. P. Mok et al., “Measuring the network performance of google cloud platform,” Proc. ACM IMC, 2021
Cellular
Applications
Characterization
Notes: Other takeaways
No daily patterns
No difference between premium and standard
Need the edge for killer apps
B5G networks need clouds deployed on public networks they don’t control and sjould account for that

## Slide 29: Future Work – Work In Progress
Notes: Fact checking our methodology
………. Against other RIPE ATLAS datasets
……different granularity and measurement types
…Under review

## Slide 30
Thank you!
Questions?
This work is supported by the project AEON-CPS (TSI-063000-2021-38), funded by the Spanish Gov. and the NextGeneration-EU plan
Notes: I thank you all for your attentions
Any Questions ?

## Slide 31: Literature
  N. Mohan et al., “Pruning edge research with latency shears”, HotNets, 2020
    Measurement and reachability of cloud centers --- Open dataset
    7 cloud providers (AWS, Google, Azure, Digital Ocean, Linode, Alibaba, Vultr)
    Use RIPE Atlas (as us) -> In Spain, they use 32 probes
    Ping every 3 hours, for 9 months, 100 cloud regions
  F. Palumbo et al., “Characterization and analysis of cloud-to-user latency: The case of Azure and AWS,” Computer Networks, 2021
    AWS and Azure --- Open dataset
    Ping every 1 minute, 25 probes, 14 days
    Several methods (ICMP, TCP, HTTP), similar results