## Slide 1: SCION: SECURE PATH-AWARE INTERNET ROUTING FOR CRITICAL INFRASTRUCTURES
Kevin Meynell, SCION Association <kme@scion.org> SEE 13, 8 April 2025

## Slide 2: THE ROUTING PROBLEM
Border Gateway Protocol (BGP): the Internet routing protocol
The current Internet routing system is inherently based on unverified trust between networks and does not have predictable route propagation.
No built-in validation that route advertisements are legitimate – in the absence of RPKI and ROV, any network can announce any ASN or IP prefix and thereby cause traffic to be re-routed (route leaks and hijacks)
Sending and receiving networks typically cannot decide the path that intermediate routers direct their traffic across the Internet
BGP can send traffic through different jurisdictions thereby creating opportunities for surveillance, compromising security and making regulatory compliance complex
BGP failover is relatively slow with convergence times of up to 3 minutes

## Slide 3: INTERNET ROUTING: WHAT ARE THE PROBLEMS?
EVENT | EXPLANATION | REPERCUSSIONS | EXAMPLE
ROUTE LEAK | Usually accidental but sometimes malicious redirection of traffic through an unintended path. A network operator with multiple links announces to an upstream provider that it has a route to a destination through another link. | Traffic is delayed or never delivered, with the intermediate network(s) carries unintended traffic. Can be used for MITM including traffic inspection and/or modification. | In Jun 2019, Verizon accepted incorrect routes from DQE Communications that diverted traffic destined for Cloudflare, Facebook & Amazon through small ISP.
ROUTE OR PREFIX HIJACKING | A network operator or attacker impersonates another network operator by falsely announcing ownership of IP prefixes and/or ASNs. Re-routes traffic by offering a shorter or more specific path for malicious or censorship reasons. | Traffic is forwarded to the wrong destination. Can be used for Denial-of-Service attacks, traffic interception or network masquerading. | Feb 2022 – KLAYswap Cryptocurrency hijack Apr 2018 - Amazon Route 53 hijack Feb 2008 - YouTube hijack
DATA SOVEREIGNTY BREACHES | BGP routing can, and often does, send traffic across geopolitical boundaries. | Can breach national and supra-national (e.g. GDPR) data protection legislation. | May 2023 – Australian healthcare data transferred through another country.
Some info @ a glance

## Slide 4: HOW IS THIS BEING ADDRESSED?
EVENT | EXPLANATION | LIMITATIONS
RPKI & ROV Resource Public Key Infrastructure & Route Origin Validation | ROAs (Route Origin Authorisations) provide cryptographic assertions of IP prefix ownership and which ASNs are allowed to originate them. Routers can validate ROAs and generate appropriate route filters. | Requires widespread deployment to be effective (less than 50% of IP prefixes are signed in 2024) Few network operators currently use ROV (5%). Only does origin validation and does not validate paths through the Internet.
BGPSEC BGP Security | Builds on RPKI to provide cryptographic assertions that every router (hop) en-route to a destination has authorized the advertisement of that route. Prevents unauthorised insertion of ASNs into a path to circumvent RPKI. | Needs to be explicitly supported by all routers along a path to achieve full benefits. Computationally intensive and introduces significant delays in route convergence. Explicit path selection is not possible. Almost no deployment.
ASPA Autonomous System Provider Authorization | ASPA objects are similar to ROAs, but allow ASNs to authorize other ASNs to carry their traffic through the Internet. Works out-of-band so doesn’t need to be deployed on all routers. | Developmental stop-gap technology and not yet an Internet standard. Does not provide assurances that traffic will actually follow validated paths.
SCION | Inter-domain routing architecture offering secure path awareness and selection. | Needs to be supported by border routers.
Some info @ a glance
?

## Slide 5: CRITICAL INFRASTRUCTURE
Legacy infrastructure needs replacing
Area Control Centers
Aircraft
Terminal Control Centers
Phone
Airline Operational Control Centers
Eurocontrol
Receives flight plans and assigns slots
Flight Plans: OLDI Protocol
and Phone
RADAR, ILS
Airport Tower & Apron
Many critical infrastructures in power, transport, emergency services etc.. run on legacy infrastructures
Many important legacy infrastructures are still not fully networked and/or are not IP based
It is expensive, inefficient and becoming harder to support these legacy infrastructures
The Internet is now able to provide sufficiently reliable and resilient connectivity, like the power grid
Critical infrastructure operators want to take advantage of commodity Internet services as they offer cost and resilience advantages, but higher trust and data sovereignty assurances are required
True inter-domain and multi-ISP support is highly desirable or required
Star centered around Area Control Centers
Radar & ILS physically connected to control towers
No connectivity between Control Centers beyond phone
Aircraft can only be managed within radio range of Control Center (so cannot be slowed/speed-up by destination)
OLDI protocol is based on data layer similar to RS232
Aircraft transponders can be spoofed and jammed
Limited coordination means inefficient management of slots
System heavily reliant on closed loop and implicit trust
Example: Air Traffic Control
P2P
P2P
Radio
Radio
Slots: OLDI Protocol
P2P links

## Slide 6: FACTS ABOUT SCION
SCION works with the existing Internet, but aims to address some of the shortcomings of BGP for particular users.
SCION introduces the concept of trusted ASes and provides greater assurances about inter-domain path security, whilst offering interoperability with the wider Internet as required.
Dispelling the Myths
Is SCION just an experimental technology for researchers?
SCION is already deployed and actively used in production networks including SSFN, SSHN & SCIERA (which is used by research and education networks).
SCION has commercial and open source implementations.
The SCION specification is being documented at the IETF.
SCION is actively being evaluated by the financial, healthcare, power utility, government, defence, aviation and rail sectors, and is also being considered for time distribution networks.
Several ISPs and IXPs are considering deployment.
Is SCION trying to replace the Internet?
What are the main use cases for SCION?

## Slide 7: WHAT IS SCION?
SCION is a resilient multi-domain path-aware architecture
SCION provides benefits similar to leased lines, but in a resilient multi-operator and multipath environment.
ENHANCED TRUST
Establishes trust domains with self-governance model that are not reliant on third-party Certificate Authorities (such as RPKI)
ASes are admitted and verified with X.509 certificates
PATH CONTROL
Source endpoints select paths across SCION-enabled ASes
Paths can be selected based on requirements (e.g. latency)
Geofencing & Hijacking prevention
MULTI-PATH DISCOVERY & FAILOVER
Fast path switching when connections fail (in ~RTT)
Multiple paths can be used simultaneously
ISP
AS8
ISP
AS1
ISP
AS2
ISP
AS4
ISP
AS3
ISP
AS5
ISP
AS6
ISP
AS7
Cloud
Office
Office
Remote Users

## Slide 8: TRUST-ENHANCED NETWORKING
Trust model is based on Isolation Domains (ISDs)
  An ISD is a logical grouping of ASes sharing a uniform trust environment (e.g. a common jurisdiction)
  Each ISD is administered by one or more Voting ASes
  Every ISD has its own trust root specified in the Trust Root Configuration - a collection of X.509 certificates with ISD information
  TRC is negotiated by the Voting ASes according to its own trust policy
  Not reliant on third-party CAs
  The CAs in an ISD can only create certificates for ASes in their respective ISD
  Each ISD must have at least one Core AS to initiate path discovery and construction (which may also be Voting ASes)
ISDs are the building blocks of SCION
Voting AS
Certificate Authority AS
Intra-ISD connection
Inter-ISD connection
ISP AS4
ISP AS5
ISP AS3
ISP AS7
Core ASes
ISP AS1
ISP AS2
ISD1
Core ASes
ISP AS12
ISP AS10
ISP AS13
ISP AS14
ISP AS11
ISD2
ISP AS8
ISP AS9
ISP AS6

## Slide 9: HOW IT WORKS
SCION core components in a nutshell
DATA PLANE – PACKET FORWARDING
Combine path segments into end-to-end path (ISD-AS level)
SCION packets contain end-to-end ISD-AS path
Border routers forward SCION packets to next SCION router or end destination based on end-to-end path
CONTROL PLANE - BEACONING
Establishes paths based on AS rather than prefixes
Beacon server uses path segment construction beacons (PCBs) to build path segments and routing paths
Path server stores paths to AS discovered during beaconing
Endpoints combine path segments to form end-to-end paths
PKI authenticates path information
0
Q
R
D
G
E
H
N
O
K
L
B
Core
Core
Core
AS
Isolation Domain (ISD)
Grouping of Autonomous Systems (AS)
Each ISD has its own trust root
Isolates AS control planes and reduces communications overhead
F➔C➔A
A➔I➔J➔M
M➔P➔S
Packet P1
Payload
Packet from AS F to AS S
A
I
J
C
P
M
F
S
ISD
ISD
ISD

## Slide 10: DEPLOYMENT MODEL
Border router
C
Control Services
Internal router
AS
C
CONTROL SERVICES (PER AS)
Beacon server – propagates and receives PCBs to construct path segments and routing paths
Path server – store mappings of AS to path discovered during beaconing
Certificate server – caches copies of TRCs and AS certificates and key management for inter-AS comms
SCION ROUTERS
SCION routers are set up at the borders of an AS
Border routers peer with other SCION-enabled networks and collect customer traffic
Control services discover, map and validate network paths
No change to the internal network infrastructure needed
Endpoints run a SCION stack
Legacy endpoints can use SCION gateways
SCION Service Provider

## Slide 11
ENTERPRISE DEPLOYMENT
SIGs support communication between IP-based hosts that are not running SCION
SIGs tunnel IP over SCION networks and allow existing networks to be integrated with SCION
SIGs can protect against DDoS attacks and malicious traffic by only allowing traffic to/from authorized Ases
SIGs can render networks invisible to anyone outside of the trusted ASes within a SCION network, therefore reducing potential attack surfaces
SIGs can be configured with path selection and failover policies
No changes to internal networks required
ISP AS4
ISP AS3
ISP AS5
ISP AS2
ISP AS1
ISP AS6
ISP AS7
ISP AS8
Example SCION IP Gateway Deployment
Data Centre
G
Head Office
G
G
G
Remote User
S
SCION link
IP Link
SCION Router
SCION IP Gateway
Internet
Remote User
Remote User
S
G
S
Integrating IP networks and hosts with SCION
SCION IP GATEWAYS

## Slide 12: SCION BENEFITS: FAST MULTI-PATH DISCOVERY & FAILOVER
BGP generally selects routes based on ‘lowest cost’ regardless of whether these are in practice the most optimal or they meet particular requirements.
With SCION, only Core ASes initiate beacons. Leaf ASes only receive and do not forward beacons.
Beaconing does not rely on iterative convergence nor forwarding table updates, allowing rapid path exploration within ISDs.
The control services discover path segments and assemble these into available paths.
Tests show path failover to be within 1-2 seconds.
Applications can choose paths based on optimal characteristics or other parameters, and can also use multiple paths simultaneously.
Advantages over regular Internet

## Slide 13: REAL-WORLD DEPLOYMENT: SECURE SWISS FINANCE NETWORK (SSFN)
Swiss inter-banking network among 300+ finance institutions, handling ~200 billion CHF/day worth of transactions between banks and other critical real-time financial services
Governed by the Swiss National Bank and SIX
Enforceable governance with SCION’s trust concept
Multi-ISP
Performance-based routing & fast failover
Geofencing
REASONS FOR USING SCION:

## Slide 14
REAL-WORLD DEPLOYMENT:
FINANCE, HEALTHCARE, POWER & EDUCATION
The Secure EFTPOS Network (SEPN) leverages SCION technology to deliver unmatched resilience, security, and flexibility in cashless payments.
PAYMENTS
HIN adopts SCION to interconnect Swiss hospitals and thousands of doctors.
HEALTHCARE
The Association of Swiss Electricity Companies has completed the concept for the Secure Swiss Utility Network (SSUN).
This is a community network, designed to integrate validated ecosystem and industry platforms, cloud applications, BPO providers, IoT, technicians, remote workers, security operation centers, and more…
POWER
The SCION Education, Research & Academic Network (SCIERA) connects campuses with path-aware high performance SCION connectivity
EDUCATION

## Slide 15: SSFN DEPLOYMENT EXPERIENCES
WHY WAS SCION ADOPTED?
SIX clients previously used Finance IPNet or point-to-point connections. Finance IPNet was reaching end-of-life.
IPNet did not limit connections to the rest of the Internet (e.g. no route controls) and offered limited protection against cyber risks.
Point-to-point connections lacked flexibility and had single points of failure.
Lacked strong governance and geofencing.
LESSONS LEARNED
Establishment of an ISD requires the creation of admission criteria, process documentation, and legal agreements.
Initial establishment of ISDs requires key-signing ceremony involving voting ASes.
Manual checks are needed when onboarding candidate ASes to ensure they meet admission criteria.
Building the PKI and management integration of the services was challenging (although SSFN offers managed service).
Certificate revocation not possible, although they expire within 72 hours.
SCION products are still relatively new and not all features are implemented yet.
Inter-ISD path control is currently limited.
The community and sources of expertise are currently limited.
Practical experience has been that path failover and fallback occurs within a few seconds.

## Slide 16: COMPARING SCION WITH OTHER SOLUTIONS
EVENT | EXPLANATION | LIMITATIONS
MPLS Multi-Protocol Label Switching | Provides high reliability and low latency routing with path selection, traffic prioritization, QoS and VPN capabilities. Has isolated control planes and infrastructure that offer DoS protection. | Connectivity is only possible over a single ISP. Designed for point-to-point connectivity so less suited to cloud environments. Requires dedicated infrastructure so unsuitable for many edge locations and remote users. MPLS deployment is declining.
SD-WAN Software-Defined Wide Area Networking | Allows secure private networks to be built using commercially available Internet access provided by different ISPs. Offers some resilience, traffic prioritization and QoS capabilities. | Connectivity is dependent on the underlying Internet connections and thus vulnerable to DoS attacks Each vendor has its own proprietary standards which limit interoperability and encourage vendor lock-in. Limited path control capability.
Segment Routing | Works over multiple ISPs and does not need to be supported by all routers on a path. Offers path control capability, faster path convergence, and traffic prioritization. | Requires MPLS or IPv6 networks. Connectivity is only possible over limited domains. Limited vendor support and interoperability. Lack of cryptographic verification of paths. Configuration and management is complex and requires understanding of underlying networks.
Why not use MPLS, SD-WAN or Segment Routing?

## Slide 17: INTERNET ENGINEERING TASK FORCE
Open specifications are important for interoperability and to encourage other implementations
SCION core components and functionality are documented in 3 Internet Drafts
Currently under review in the IETF Independent Submission Stream
Specification Internet Drafts:
SCION PKI draft-dekater-scion-pki
SCION Control Plane draft-dekater-scion-controlplane
SCION Data Plane draft-dekater-scion-dataplane

## Slide 18: COMMERCIAL & OPEN-SOURCE IMPLEMENTATIONS
If you’re interested in deploying SCION, there are currently two options:
Commercial
Open Source
Other implementations under development: P4, Rust, OpenWRT
SCION Association formed by deployers and early adopters to support open source development, standardization, and community involvement.

## Slide 19: THE SCION ASSOCIATION
COMMUNITY
Raising awareness of SCION, promoting the benefits and encouraging adoption, developing its community, and providing marketing support to implementors and deployers
STANDARDIZATION
Developing the specifications to implement SCION, with the goal of making it an interoperable Internet standard
OPEN SOURCE
Maintaining and coordinating the SCION implementation for research, development, and experimental deployments
Promoting openness and collaboration to unlock the full potential of SCION
Non-profit association established in 2022
Open for membership to all entities interested in SCION
https://www.scion.org

## Slide 20: SCION TODAY
A growing ecosystem
Vendors, Integrators
Research
Users
ISPs

## Slide 21: THANK YOU!
More information:
The Complete Guide to SCION
Springer Verlag, 2022
SCION Association: https://www.scion.org
Reference & Developer Docs: https://docs.scion.org/
Research: https://scion-architecture.net
Vendor: https://www.anapaya.net/resources
Latest Release: https://github.com/scionproto/scion/releases/