## Slide 1
RIPE South East Europe 13th Meeting - Sofia
April 7-8, 2025
20 years R&E monitoring
Ivan Garnizov, BREN
pS DevTeam WP6T3 and pS system engineer for NOC WP9T2 in GÉANT GN5-2
Horizon Europe
programme

## Slide 2
Paul can we have an agenda slide?
Organisation, environment, focus and challenges
The perfSONAR platform and features
Measuring of 400Gb/s and above
A glance in the near future
Resources
Agenda

## Slide 3: The GÉANT Network
Interconnects research, education and innovation communities worldwide, with secure, high-capacity networks.
Total Backbone Trunk Capacity
12.8 Tbps
38 European National Research and Education Networks + NORDUnet ( 5 Nordic NRENs)
over 10,000 institutions and 50 million academic users.

## Slide 4: At the heart of global research and education networking
CERN
EOSC
SKAO
PRACE
Belle II
EuroHPC
ITER - Fusion Research

## Slide 5
Problem Statement: make data flow
The global Research & Education network ecosystem
This complex, heterogeneous set of networks must operate seamlessly from “end to end”
Data mobility is required

## Slide 6: Where Are The Problems?
Source
Campus
Backbone
NREN
Congested or faulty links between domains
Congested intra- campus links
Destination
Campus
Latency dependant problems inside domains with small RTT
Regional
???
???

## Slide 7: Very small packet loss and TCP performance
No Loss
Loss of 1 packet per 20.000

## Slide 8: What is perfSONAR?
8
An open source software collaboration
A platform for network monitoring and measurements across organizations on various quality parameters
Network specific measurements
  Throughput
  One-way delay
  Jitter
  Packet Loss
  Traceroute
  RTT
  2 more ?
  Network metrics challenge

## Slide 9
Released October 17 2024
Grafana Interface
  Customizable visualization, better integration with other data
Threaded iperf3 Support
  Ability to test at 100Gbps+
Python pSConfig
  Better maintainability of more modern codebase
Better Instrumentation and Troubleshooting Tools
  Makes it easier to identify issues when perfSONAR misbehaves
More recent OS Support
  Debian 11, Debian 12 and Ubuntu 22 support. On top of EL9 (Alma, Rocky) and Ubuntu 20.
5.1.4

## Slide 10: The Fundamentals

## Slide 11: New UI: Instrumentation

## Slide 12: New UI: Focus on Measurements

## Slide 13: New UI: MaDDash Integration

## Slide 14: Analytic plugins by NetSage and ESnet

## Slide 15: What is iperf3?
iperf3 is an open-source tool that measures network traffic performance between a client and server
It was designed to be used in perfSONAR, but can also be used on its own
Linux, MacOS, and FreeBSD are all officially supported

## Slide 16: iperf3 Multi-Threading
Before multi-threading, iperf3 was capable of 30-50 Gbps, with single stream TCP, possibly more with tuning
Many links are faster than iperf3
  Site connections: N x 100G
  Backbone: 400G +
So what if we want to support connections with higher bandwidth? How do we get more throughput?
The problem: Adding more parallel connections doesn’t increase throughput
Solution: Adding multi-threading to iperf3 to use multiple CPU cores

## Slide 17: Effects on Performance
Internal testing showed that iperf3-mt has significant improvements in throughput performance over iperf3
iperf3-mt
iperf3

## Slide 18: LS dashboard refreshment
https://stats.perfsonar.net/

## Slide 19: 20 years of experience

## Slide 20: 20 years of experience…
April 2025
Source: https://www.perfsonar.net/about_history.html

## Slide 21: Usecases
Materials used
  SKA Regional Centre Network Technical Roadmap- Network needs, Distributed Data Management - Rosie Bolton (Aula Magna) LHCOPN-LHCONE meeting #52 - INFN Catania IT 04.2024
  BelleII update - Silvio Pardi (Universita Federico II e INFN Sezione di Napoli (IT) LHCOPN-LHCONE meeting #52 - INFN Catania IT 04.2024
  Belle II Network Overview, Malachi Schram1, Silvio Pardi2, Soh Suzuki3, Takanori Hara3 LHCONE Meeting – Berkeley, 06.2015
  perfSONAR in the WLCG, Duncan Rand, Imperial College London First European perfSONAR meeting, London, June 2019

## Slide 22: The Future of perfSONAR

## Slide 23: perfSONAR 5.2.0 (April 2025) and 5.3.0 (Q4 2025)
psCompose: Improving test configuration experience
On-demand measurement UI
Lookup service enhancements
Micro-dependency analysis
Support of new Linux distributions

## Slide 24: What comes next?
Operational analysis and alarming
  Leverage features of current technology stack
  Better orchestration of debugging process
  Integration with existing data, processes and projects (e.g. MetrANOVA)
  Explore possibilities in AIOps for identifying relevant measurements
Training the community on the new generation of perfSONAR
  Update our perfSONAR channel on YouTube
  Organize workshop events for the community: USA and Europe

## Slide 25: Installation quick start
Install instructions are > here
New install script (to run as root):
Bundle options > here
Install Instructions
https://docs.perfsonar.net/install_quick_start
curl -s https://downloads.perfsonar.net/install | sh -s - toolkit

## Slide 26: Additional Resources
perfSONAR Website http://www.perfsonar.net/
perfSONAR Documentation http://docs.perfsonar.net/
Lookup Service Dashboard https://stats.perfsonar.net/
YouTube Channel https://www.youtube.com/perfSONARProject
FasterData Knowledge Base http://fasterdata.es.net/

## Slide 27: 20 years R&E monitoring
Ivan Garnizov • BREN / GÉANT WP6T3 and WP9T2 • i.garnizov@cc.bas.bg
Network metrics challenge
Questions?